Blinky Color POV Parts rev 2
100nF Capacitor / (C1, C3, C4, C6)	1uF Capacitor( C5, C7, C8) / marked “105” in tiny print / Need 3 of these	10uF Capacitor (C2) / marked “106” in tiny print / With a black dot
10k Resistor (R1, R4, R5)	4.7k Resistor (R2, R3)	LED (D1-D8)
Connector (Optional) P2	Connector (Optional) P1	Light sensors (D9, D10)
Switch (SW1)	Push button (SW2)	Voltage regulator (U1)

Battery Case	Red and Black Wires	IC Socket
Circuit Board

# Directions.....
1. Solder in the resistors / R2 and R3 are 4.7k / Yellow, Violet, Red, Gold / R1, R4 and R5 are 10k / Brown, Black, Orange, Gold
2. Solder in the capacitors / C2 is 10uF “106” / C5, C7, C8 are 1uF “105” / C1, C3, C4, C6 are 0.1uF “104”
3. Solder in the IC socket / IC1 / Be sure the notch is the same way up as the mark on the board!
4. Solder in the power switch / SW1
5. Solder in the Programming Button / PROG
6. Solder in the voltage regulator / U1 / Make sure it goes the right way around, / with the metal tab towards U2
7. Solder in the light sensors / They have to go the right way around / The long lead goes in the round pad / The short lead goes in the square pad / Bend them so they stick out and are / about the same length, as shown
8. Solder in the LEDs / These are tricky. They have 4 leads. / The side with the black dot goes up / towards the top of the board / (where the light sensors are)
9. Attach the wires to the battery holder Solder the red and black wires to the battery holder as shown. Be sure the red wire is connected to the pin near the corner. / Solder the other end of the wires into the circuit board. The red wire goes into the “+”hole

You're done!

Inspect your work carefully, and get your helper to check it out, too.

Then, go ask for batteries and a microcontroller and you're ready to try out your BlinkyColorPOV!